# 01 - Configuration
## SDDS-STS-SRS-ESPACE-TBD01-001
Test Description
The test verifies that on the ESPACE tool, in the “Password” tab panel the sub panel “SDDS Users password rules” is present and the SDDS Administrator is allowed to configure the minimum password length for all the SDDS User and to save the configuration.
This test envisages a manual qualification method.
The scenario foresees an ESPACE tool running.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-TBD02-001
Test Description
The test verifies that on the ESPACE tool, in the “Password” tab panel the sub panel “SDDS Users password rules” is present and the SDDS Administrator is allowed to enable or disable the possibility of using an empty password for all the SDDS User and to save the configuration.
This test envisages a manual qualification method.
The scenario foresees running the ESPACE tool.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.
## SDDS-STS-SRS-ESPACE-101-001
Test Description
The test verifies that the ESPACE allow to specify:
   Number of CORE BBs belonging to the SDDS system to be configured;
   Number of additional WKS belonging to the SDDS system to be configured.
According to SDDS constraint the following maximum deployment is permitted:
Number of CORE BBs is up to 20;
Number of additional WKSs is up to 3.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.
## SDDS-STS-SRS-ESPACE-104-001
Test Description
The test verifies that the ESPACE preserve the minimum SDDS configuration, consisting of:
- a CORE BB, made up of two Units;
- a MNG BB, made up of two Units.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-106-001
Test Description
The test verifies that the ESPACE allow to specify the hardware type for each:
SDDS CORE BB,
SDDS MNG BB,
additional WKS (if any).

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-108-001
Test Description
The test verifies that the ESPACE allow to configure the following settings for each CORE BB belonging to the SDDS system to configure:
Bonding
IP Addresses
Hosts File
Alive Messages
User LANs
Reverse path Filter
Passwords
NTP
IPSec
Once the configuration is accomplished (i.e. creation or modification) the user can save the new tar archive.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.+
## SDDS-STS-SRS-ESPACE-111-001
Test Description
The test verifies that the ESPACE allow to configure the following settings for MNG BB belonging to the SDDS system to configure:
Bonding
IP Addresses
Hosts File
Workstation auto start
Passwords
NTP
IPSec
Once the configuration is accomplished (i.e. creation or modification) the user can save the new tar archive.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.
## SDDS-STS-SRS-ESPACE-114-001

Test Description
The test verifies that the ESPACE allow to configure the following settings for each additional WKS belonging to the SDDS system to configure:
- IP Addresses
- Hosts File
- Workstation auto start
- Passwords
- NTP
- IPSec
Once the configuration is accomplished (i.e. creation or modification) the user can save the new tar archive.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-117-001
Test Description
The test verifies that the ESPACE allow to load an existing configuration (TAR File) and to display the settings contained XML files.

Environmental needs
None.

Preparatory Actions
Download ESPACE_SDDS_CONF.tar in Attachments.

Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-119-001
Test Description
The test verifies that ESPACE uses the default configuration if no settings are specified.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-121-001
Test Description
The test verifies that the ESPACE, upon manual SDDS User action of saving the configuration, save the configuration by producing a tar archive containing XML files.
When saving the configuration, the SDDS User can also overwrite an existing file.
The tar archive is saved with a version tag.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-124-001
Test Description
The test verifies that the ESPACE allow the SDDS User to customise an SDDS SR USB stick by means of:

selection of a SDDS USB stick;
selection of a Configuration Set;
enclosement of the selected files by creating a single tar archive stored in the selected destination folder.

Environmental needs
None.

Preparatory Actions
Download "SDDS_INSTL_06.02.tar", "CS_1-SR_06.02.tar" and "CS_1-SR_06.02.tar.md5" file in the attachments.

Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.
## SDDS-STS-SRS-ESPACE-55-001
Test Description
The test verifies that the ESPACE provides the SDDS User with a Graphic User Interface.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.
## SDDS-STS-SRS-ESPACE-95-001
Test Description
The test verifies that the ESPACE provides the SDDS User with an application that runs on platforms offering an Operating System based on Linux.

Environmental needs
None.

Preparatory Actions
Run the test on a platform offering an Operating System based on Linux.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-95-002
Test Description
The test verifies that the ESPACE provides the SDDS User with an application that runs on platforms offering an Operating System based on Windows.

Environmental needs
None.

Preparatory Actions
Run the test on a platform offering an Operating System based on Windows.
To start ESPACE application on Windows, double click on startEspace.bat file.
## SDDS-STS-SRS-ESPACE-97-001
Test Description
The test verifies that the ESPACE provides the SDDS User with the following functions:
New configuration, aiming at create a new configuration;
Load configuration, aiming at display and edit an existing configuration;
Save configuration, aiming at confirm the changes on the current configuration;
Customisation of SDDS SR USB stick, aiming at enclose an SDDS SR USB stick and a Configuration Set in a single tar archive.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-99-001
Test Description
 The test verifies that the ESPACE provides the SDDS User with a step-by-step procedure in order to create a new configuration.
The step-by-step procedure is providing the following functions to navigate among the available functions:
- Next, to display the next setting (if available) and which is possible if all entries specified by the user are consistent;
- Previous, to go back to the previous step (if available);
- Cancel, to close the procedure at any stage of the configuration.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 02- bonding
## SDDS-STS-SRS-ESPACE-126-001
Test Description
The test verifies that the ESPACE allow the SDDS User to specify, in "Bonding" tab, for each SDDS CORE BB and MNG BB the network interfaces:
ILAN
    Interface 1 (mandatory field)
    Interface 2 (mandatory field)
IWAN
    Interface 1 (mandatory field)
    Interface 2 (mandatory field only for MNG BB)
ELAN
    Interface 1 (mandatory field)
    Interface 2 (mandatory field only for MNG BB)

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-128-001

Test Description
The test verifies that the ESPACE, upon manual user action of confirming the “Bonding” configuration:
- prevent confirmation of the configuration by displaying an error message if at least one of the mandatory interface (according to the current BB type) is missing or already in use;
- confirm the configuration otherwise.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 03 – ip addresses
## SDDS-STS-SRS-ESPACE-130-001
Test Description
The test verifies that the ESPACE allow the SDDS User to specify the IP Addresses configuration for each SDDS Building Block and Additional WKS.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-132-001
Test Description
The test verifies that the ESPACE allow the SDDS User to specify the following IP Addresses configuration for each SDDS CORE BB and for the SDDS MNG BB:
ILAN
  1. IP Address, for both Unit A and Unit B;
  2. Netmask;
  3. Gateway;
  4. Virtual IP Address;
  5. Virtual IP Netmask;
IWAN
  1. IP Address, for both Unit A and Unit B;
  2. Netmask;
  3. Gateway;
  4. Virtual IP Address;
  5. Virtual IP Netmask;
ELAN
  1. IP Address, for both Unit A and Unit B;
  2. Netmask;
  3. Gateway;
  4. Virtual IP Address;
  5. Virtual IP Netmask;
Default Gateway.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-134-001
Test Description
The test verifies that the ESPACE, upon manual user action of confirming the “IP Addresses” configuration for each Unit belonging to SDDS CORE BB or SDDS MNG BB:
prevent confirmation of the configuration by displaying an error message if at least one of the following checks fails:
  - IP address does not match with the IP Address pattern;
  - Netmask does not match with the Netmask pattern;
  - Default gateway does not match with the IP Address pattern;
  - CORE Unit A and CORE Unit B IP addresses consistency check;
  - IP addresses check among all configured LANs;
confirm the configuration otherwise.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-136-001
Test Description
The test verifies that the ESPACE, upon manual user action of confirming the “IP Addresses” configuration of additional WKS:
- prevent confirmation of the configuration by displaying an error message if at least one of the following checks fails:
  - IP address does not match with the IP Address pattern;
  - Netmask does not match with the Netmask pattern;
  - Network Interface does not match with the IP Address pattern;
  - ILAN and IWAN interfaces are the same;
  - ILAN and IWAN IP addresses are the same;
  - Default gateway does not match with the IP Address pattern;
  - IP addresses check among all configured LANs (i.e. if IP addresses are already in use by other items).
confirm the configuration otherwise.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-138-001
Test Description
The test verifies that the ESPACE allow the SDDS User to specify the following IP Addresses configuration for each additional SDDS WKS:
ILAN:
  1. IP Address
  2. Netmask
  3. Network Interface
IWAN:
  1. IP Address
  2. Netmask
  3. Network Interface
Default Gateway

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 04 – hosts file
## SDDS-STS-SRS-ESPACE-140-001
Test Description
The test verifies that the ESPACE, if the “Hosts File” function is selected, allow the SDDS User to handle (i.e. add, edit and remove) hosts by specifying:
- Host name;
- IP Address.

In case of a new configuration, the default list is displayed according to the specified BBs/additional WKSs. The following hosts are suggested for a basic configuration:
- CORE virtual server, default host name “sdds-core-bb1-virtual”;
- CORE 1A, default host name “sdds-core1”;
- CORE 1B, default host name “sdds-core2”;
- MNG virtual server, default host name “sdds-mng-virtual”;
- MNG 1A and to WKS1 (which is embedded on MNG Unit), default host name “sdds-mng1 sdds-wks1”;
- MNG 1B and to WKS2 (which is embedded on MNG Unit), default value “sdds-mng2 sdds-wks2”;
- 1st router, default host name “sdds-rt1”;
- 2nd router, default host name “sdds-rt2”;
- 1st switch, default host name “sdds-sw1”;
- 2nd switch, default host name “sdds-sw2”;

Furthermore, the following BB type can be configured:
- Router 3rd, default host name “sdds-rt3 default name”;
- Router 4th, default host name “sdds-rt4 default name”;
- Storage server, default host name “sdds-storage-server”;
- Other type.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-143-001
Test Description
The test verifies that the ESPACE, upon manual user action of confirming the “Hosts File” configuration:
- prevent confirmation of the configuration by displaying an error message if:
  - Host name or IP Address is empty;
  - the provided Host name exceeds 20 characters;
  - the provided IP Address does not match with the IP Address pattern;
  - the provided IP Address is already in use for another Host name;
  - the provided Host name already exists;
confirm the configuration otherwise.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 05 – alive messages
## SDDS-STS-SRS-ESPACE-145-001
Test Description
The test verifies that the ESPACE, allow the SDDS User to enable (default value) or disable the Alive messages exchange on IWAN and ELAN for each SDDS CORE BB.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-147-001
Test Description
The test verifies that the ESPACE, allow the SDDS User to enable or disable (default value) the Alive messages exchange on XLAN for each SDDS CORE BB.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-149-001
Test Description
The test verifies that the ESPACE, if the “Alive messages” function is selected and the Alive messages exchange on XLAN is enabled for the current SDDS CORE BB, allow to configure the XLAN by specifying the following:
- IP Address of the Unit A of the selected CORE BB;
- IP Address of the Unit B of the selected CORE BB;
- Netmask;
- Network interface.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-151-001
Test Description
The test verifies that the ESPACE, upon manual user action of confirming the “Alive messages” configuration and if the XLAN setting up is specified:
- prevent confirmation of the configuration by displaying an error message if:
  - the setting up is not completed (i.e. at least one field is missing);
  - the provided ‘IP Address’ does not match with the IP Address pattern;
  - Netmask does not match with the Netmask pattern;
  - both IP Addresses contain the same value;
  - network interface is not selected.
- confirm the configuration otherwise.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 06 – user LANs

## SDDS-STS-SRS-ESPACE-153-001
Test Description
The test verifies that the ESPACE allow the SDDS User to define on a single CORE BB up to twelve (12) User LANs configured as LAN in addition to the System LANs (i.e. ILAN, IWAN, ELAN and XLAN) by using any available Network Interface.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-155-001
Test Description
The test verifies that the ESPACE allow the SDDS User to define on a single CORE BB up to ten (10) User LANs configured as VLAN per Network Interface, not assigned to System LANs (i.e. ILAN, IWAN, ELAN and XLAN).

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-157-001
Test Description
The test verifies that the ESPACE allow the SDDS User to configure up to one hundred and twenty (120) User LANs (LAN and/or VLAN configurations).

Environmental needs
None.

Preparatory Actions
Download ESPACE_SDDS_CONF_120LAN.tar in Attachments.

Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-159-001
Test Description
The test verifies that the ESPACE prevent from assigning the Network Interfaces used for ILAN to any other LAN.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-161-001
Test Description
The test verifies that the ESPACE prevent from assigning the Network Interfaces used for IWAN to any other LAN.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-163-001
Test Description
The test verifies that the ESPACE prevent from assigning the Network Interfaces used for ELAN to any other LAN.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-165-001
Test Description
The test verifies that the ESPACE prevent from assigning the Network Interfaces used for XLAN to any other LAN.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-167-001
Test Description
The test verifies that the ESPACE allow the SDDS User to decide for which LAN and/or VLAN bonding interfaces have to be used.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-169-001
Test Description
The test verifies that the ESPACE allow the SDDS User to specify for each User LAN individually whether a CORE switchover has to be triggered in case that User LAN changes status to unavailable.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-171-001
Test Description
The test verifies that the ESPACE allow the SDDS User to assign a name to the User LAN.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-173-001
Test Description
The test verifies that the ESPACE allow the SDDS User to specify which User LAN is to be used for Data Exchange.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-175-001
Test Description
The test verifies that the ESPACE perform the following checks for all IP addresses and NETMASK fields of the User LANs configuration:
- IP address does not match with the IP Address pattern;
- Netmask does not match with the Netmask pattern;
- CORE A and CORE B IP addresses consistency check (i.e. on the same LAN and don’t contain the same values and are different from Virtual IP Address);
IP addresses check among all configured LANs/VLANs/System LANs (i.e. IP addresses are not already used by other LANs/VLANs nor by System LANs).

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 07- reverse path filter
## SDDS-STS-SRS-ESPACE-177-001

Test Description
The test verifies that the ESPACE allow the SDDS User to enable (default value) or disable the Reverse path filter on the selected SDDS CORE BB.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 08-wks autostart
## SDDS-STS-SRS-ESPACE-179-001
Test Description
The test verifies that the ESPACE allow the SDDS User to enable or disable (default value) the auto start for each SDDS WKS.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 09-passwords
## SDDS-STS-SRS-ESPACE-181-001
Test Description
The test verifies that the ESPACE allow the SDDS User the setting up of the password of the ‘sdds’ and the root users, by specifying for each one:
- Password;
- Confirm password.

Password recommendations follow:
- can reach 25 characters
- can contain alpha character [a-z;A-Z]
- can contain numeric character [0-9]
- can contain one or more of the following special characters (between double quotes): "()!<>;#_-|+:;.,%/[]{}*@"

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-184-001
Test Description
The test verifies that on the ESPACE tool, following the manual action of the user to confirm the "Password" configuration, the operation is prevented by displaying an error message if:
  - ‘Password’ or ‘Confirm password’ for the ‘sdds’ user is empty;
  - ‘Password’ and ‘Confirm password’ specified for the ‘sdds’ user do not match;
  - ‘Password’ or ‘Confirm password’ for root is empty;
  - ‘Password’ and ‘Confirm password’ specified for root do not match;
  - ‘Password length’ is out of range;
This test envisages a manual qualification method.
The scenario foresees running the ESPACE tool.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 10-ipsec
## SDDS-STS-SRS-ESPACE-186-001
Test Description
The test verifies that the ESPACE allow to configure the IPSec by specifying:
- LAN, by selecting one of the following options:
  - ILAN;
  - ELAN (Not recommended);
  - IWAN (Not recommended);
  - ILAN, ELAN (Not recommended);
  - ILAN, IWAN (Not recommended);
  - IWAN, ELAN (Not recommended);
  - ILAN, IWAN, ELAN (Not recommended).
- IPSec service automatically starts on boot, which can be enabled or disabled (default value);
- Security PRE-SHARED KEY;
- Type, which can be Transport (default value) or Tunnel;
- PHASE 1 Encryption, which can be “aes-cbc” (default value), “aer-gcm” or “3des”;
- PHASE 1 hashing, which can be “sha1” (default value) or “md5”;
- PHASE 2 Encryption, which can be “aes256” (default value) or “3des”;
- PHASE 2 authentication, which can be “sha1” (default value) or “sha2”.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-188-001
Test Description
The test verifies that the ESPACE allow the SDDS User to enable or disable (default value) the IPSec for the current SDDS configuration.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-190-001
Test Description
The test verifies that the ESPACE allow to:
prevent confirmation of the configuration by displaying an error message if:
Security PRE-SHARED KEY is empty;
confirm the configuration otherwise.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-192-001
Test Description
The test verifies that the ESPACE allow to configure the IPSec Single connection for each BB in the current SDDS by specifying:
- LAN, by selecting one of the following options:
    - ILAN;
    - ELAN (Not recommended);
    - IWAN (Not recommended);
    - Custom.
- Security PRE-SHARED KEY;
- Unit A IP Address;
- Unit B IP Address;
- Remote Peer Address;
- IPSec service automatically starts on boot, which can be enabled or disabled (default value);
- Type, which can be Transport (default value) or Tunnel;
- PHASE 1 Encryption, which can be “aes-cbc” (default value), “aer-gcm” or “3des”;
- PHASE 1 hashing, which can be “sha1” (default value) or “md5”;
- PHASE 2 Encryption, which can be “aes256” (default value) or “3des”;
- PHASE 2 authentication, which can be “sha1” (default value) or “sha2”.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-192-002
Test Description
The test verifies that the ESPACE allow to configure the IPSec Single connection for each BB in the current SDDS by specifying:
- LAN, by selecting one of the following options:
    - ILAN;
    - ELAN (Not recommended);
    - IWAN (Not recommended);
    - Custom.
- Security PRE-SHARED KEY;
- Unit A IP Address;
- Unit B IP Address;
- Remote Peer Address;
- IPSec service automatically starts on boot, which can be enabled or disabled (default value);
- Type, which can be Transport (default value) or Tunnel;
- PHASE 1 Encryption, which can be “aes-cbc” (default value), “aer-gcm” or “3des”;
- PHASE 1 hashing, which can be “sha1” (default value) or “md5”;
- PHASE 2 Encryption, which can be “aes256” (default value) or “3des”;
- PHASE 2 authentication, which can be “sha1” (default value) or “sha2”.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-192-003
Test Description
The test verifies that the ESPACE allow to configure the IPSec Single connection for each BB in the current SDDS by specifying:
- LAN, by selecting one of the following options:
    - ILAN;
    - ELAN (Not recommended);
    - IWAN (Not recommended);
    - Custom.
- Security PRE-SHARED KEY;
- Unit A IP Address;
- Unit B IP Address;
- Remote Peer Address;
- IPSec service automatically starts on boot, which can be enabled or disabled (default value);
- Type, which can be Transport (default value) or Tunnel;
- PHASE 1 Encryption, which can be “aes-cbc” (default value), “aer-gcm” or “3des”;
- PHASE 1 hashing, which can be “sha1” (default value) or “md5”;
- PHASE 2 Encryption, which can be “aes256” (default value) or “3des”;
- PHASE 2 authentication, which can be “sha1” (default value) or “sha2”.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-194-001
Test Description
The test verifies that the ESPACE:
- prevent confirmation of the configuration by displaying an error message if:
  - Security PRE-SHARED KEY is empty;
  - Unit A IP Address does not match with the IP Address pattern;
  - the ILAN is selected and the Unit A IP Address does not match with the IP Address already configured for the Unit A;
  - Unit B IP Address does not match with the IP Address pattern;
  - the ILAN is selected and the Unit B IP Address does not match with the IP Address already configured for the Unit B;
  - Remote Peer Address does not match with the IP Address pattern;
  - Unit A IP Address and Unit B IP Address are different from the Remote Peer Address;
- confirm the configuration otherwise.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

# 11- ntp
## SDDS-STS-SRS-ESPACE-196-001
Test Description
The test verifies that the ESPACE allow the SDDS User to configure the NTP server by specifying:
- Default Configuration (enabled by default);
- NTP server 1 IP Address;
- NTP server 2 IP Address.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.

## SDDS-STS-SRS-ESPACE-198-001
Test Description
The test verifies that the ESPACE, for each SDDS CORE BB and SDDS MNG BB:
- prevent confirmation of the configuration by displaying an error message if at least one of the following checks fails:
  - if the Default Configuration is not selected and the NTP server 1 IP Address does not match with the IP Address pattern;
  - if the Default Configuration is not selected and the NTP server 2 IP Address does not match with the IP Address pattern;
  - if the Default Configuration is not selected and both IP Addresses contain the same value;
- confirm the configuration otherwise.

Environmental needs
None.

Preparatory Actions
Test can be run on a platform offering an Operating System based on Windows or based on Linux.
To start ESPACE application on Windows, double click on startEspace.bat file.
To start ESPACE application on Linux, launch ./startEspace.sh script.